## Slide 1
High-Resolution Hyperspectral Microscopy for Efficient Analysis of Biological Systems
Ondřej Vaculík

## Slide 2
Masters in Optics and Optoelectronics – Palacký University Olomouc
  Multispectral image acquisition and analysis
PhD student – Brno University of Technology
  Thesis title: Advanced Spectral and Image Processing of Hyperspectral Data
Institute of Scientific Instruments of CAS
  Applied and Integrated Photonics group member (aip.isibrno.cz)
My Background

## Slide 3
Inverted configuration
Transmission spectra
Offner based imaging spectroscope
4-100x magnification (RMS/M25)
0.1 nm spectral resolution (FWHM)
120 nm bandwidth tunable in 450-900 nm range
Automated measurement and calibration (Python)
Hyperspectral Microscope System Specs

## Slide 4
Autoencoder for Spectral Dimensionality Reduction
Reducing the spectral dimension
Clustering using the encoded spectrum  processing speed up
Working with full spectrum of regions of interest
Synechocystis sp. PCC6803
Trachydiscus minutus
1µm
Autoencoder

## Slide 5
3 strains of marine cyanobacteria with different pigments
96-well microplate with 1:1, 1:2, 1:4, 1:1:1, and 1:2:3 ratios
Ratio estimation using Multivariate Curve Resolution (MCR)
(0.76±0.12)% identification accuracy
96% processing speedup when using dim. reduction (3 component NMF)
Marine Cyanobacteria Spectral Unmixing
Spectral Unmixing
G
R
Y
Mixtures
Calculated
Concentration
HS Measurement
Samples
Notes: PHOTOMACHINES - Photosynthetic cell redesign for high yields of therapeutic peptides